## Slide 1: Dr. B. R. Ambedkar National Institute of Technology
Biofuel Production using Waste oil
Submitted by: Sahil (22112068)
Saloni Garg (22112070)
Guided by:
Dr. Deepak Sahu
(Assistant Professor)

## Slide 2: INTRODUCTION

## Slide 3
Fossil fuels are depleting and cause environmental harm (pollution, climate change).
Renewable energy sources (solar, wind, bioenergy, hydrogen) are increasingly adopted.
Plastics and agricultural waste create long-term environmental problems.
Co-pyrolysis offers a sustainable solution by converting biomass and plastic waste into fuel.
Supports circular economy: reduces waste and generates energy.
Need for Waste-to-Energy

## Slide 4
Pyrolysis is the process of thermal decomposition without oxygen. It converts organic waste into bio-oil, syngas, and biochar.
Works on plastics, rubber, agricultural waste, etc.
Reduces greenhouse gas emissions and pollution.
Feedstock type and temperature significantly affect product distribution.
What is Pyrolysis?

## Slide 5
Co-pyrolysis is the process of simultaneous pyrolysis of biomass and plastic waste.
Benefits:
  Lower oxygen content, improved stability
  Reduced char, more light hydrocarbons
What is Co-pyrolysis?

## Slide 6
Abundantly available from homes and restaurants.
Cost-effective and reduce waste.
Does not compete with food crops.
Promotes circular economy.
FEEDSTOCK SELECTION

## Slide 7
Feedstock | Type | Pros | Cons
Waste Cooking Oil (WCO) | Waste/Used Oil | - Cheap or free - Reduces waste - Easily available - Eco-friendly | - Needs pre-treatment - Composition varies - May contain impurities
Soybean Oil | Edible Vegetable Oil | - High oil content - Well-studied process | - Competes with food supply - Higher cost
Palm Oil | Edible Vegetable Oil | - High yield per hectare - Widely available in tropical regions | - Deforestation issues - Competes with food
Rapeseed/Canola Oil | Edible Vegetable Oil | - Good cold flow properties - Popular in Europe | - Expensive - Food vs fuel debate
Sunflower Oil | Edible Vegetable Oil | - Readily available in many countries | - Higher production cost - Competes with food
Animal Fats (e.g., tallow) | Non-Edible Waste | - Inexpensive - Utilizes slaughter waste | - High melting point - Poor cold flow properties
Algae Oil | Non-Edible (Future) | - High yield - Grows on non-arable land - Doesn’t compete with food | - Expensive - Technology not yet commercial
Jatropha Oil | Non-Edible Plant | - Grows on marginal land - Non-food crop | - Toxic - Low and inconsistent yields
Used Industrial Oils | Waste/Non-Food | - Cheap or free - Reduces pollution | - Requires heavy treatment - May have toxic impurities

## Slide 8
Sustainable and Green
Low Cost
High Catalytic Activity
Reusability
Eco-Friendly
Catalyst selection
(zinc doped Biochar)

## Slide 9
Type of Catalyst | Examples | Type | Pros | Cons
Alkali Catalysts | NaOH, KOH | Homogeneous | - High reaction rate - Low cost | - Difficult to recover - Produces soap with FFA - Not eco-friendly
Acid Catalysts | H₂SO₄, HCl | Homogeneous | - Works with high FFA oils - Prevents soap formation | - Corrosive - Slow reaction rate - Requires long reaction time
Enzyme Catalysts | Lipase | Biocatalyst | - Mild conditions - High specificity | - Expensive - Sensitive to alcohol and temperature
Metal Oxides | ZnO, CaO, MgO | Heterogeneous | - High activity - Reusable - Environmentally safer | - Prone to leaching - Costly for some metals
Bio-waste-based Catalysts | Eggshells, bones, shells | Heterogeneous | - Abundant - Cheap - Renewable | - Impure - Variable quality
Zeolites & Solid Acids | H-ZSM-5, Amberlyst | Heterogeneous | - Good thermal stability - Reusable | - Expensive - Requires complex synthesis
Zinc-Doped Biochar | Biochar from biomass + Zn (ZnO, Zn²⁺) | Heterogeneous | - Cheap & renewable - High surface area - Reusable - Environmentally friendly | - Activity drops slightly after 3–4 uses - Needs pyrolysis setup

## Slide 10
This is the chemical reaction that converts oil into biodiesel.
Steps:
Preparation: WCO is filtered to remove impurities.
Reaction:WCO + Methanol + Zinc-doped biochar catalyst is Heated to ~60–65°C for 2–3 hours.Reaction converts triglycerides in oil into Fatty Acid Methyl Esters (FAME) – the main component of biodiesel.
Separation: Mixture separates into two layers:Top: BiodieselBottom: Glycerol + leftover catalyst
Purification:Biodiesel is washed with warm water and dried.
Properties (density, viscosity, flash point, etc.) are tested.
TANSESTERIFICATION

## Slide 11: General Reaction Equation

## Slide 12: DETAILED PROCESS

## Slide 13: Step 1 (Oil Collection and Pretreatment)
COLLECTION: waste cooking oil collected from restaurants or households.
FILTRATION: Removes food particles and solid residues.
DRYING: Removes moisture content to avoid soap formation.
RESULT: clean oil suitable for reaction.

## Slide 14: Step 2 (Catalyst Preparation)
Raw Material: Agricultural waste (e.g., rice husk) selected asbiomass.
Pyrolysis: Biomass heated at 400-500°C in absence of oxygen → Biochar.
Zinc Doping: Biochar soaked in zinc nitrate/acetate solution.
Drying and Heating: Catalyst is dried and activated by further heating.
Characterization: XRD, SEM, and EDX used to confirm structure and activity..

## Slide 15: Step 3 (Reaction Setup)
- 3-neck flask setup with condenser, thermometer, and heating mantle.
- Mixture: WCO + Methanol + Zinc-doped biochar.
- Common ratio: 6:1 methanol to oil, 4 wt% catalyst.
- Stirring ensures uniform reaction.

## Slide 16: Step 4 (Transesterification Reaction)
Heating mixture to ~60°C for 2-3 hours.
Catalyst enables breakdown of triglycerides.
Reaction yields two phases:
- Upper: Biodiesel (methyl esters)
- Lower: Glycerol and residual catalyst

## Slide 17: Step 5 (Separation of Products)
Cooling: Reaction mixture allowed to cool.
Settling: Two phases separate naturally due to density difference.
Separation: Biodiesel (top layer) decanted from glycerol (bottom layer).
Catalyst: Filtered from glycerol and reused

## Slide 18: Step 6 (Purification of Biodiesel)
Washing: Biodiesel washed with warm water to remove residuals.
Neutralization: Ensures removal of catalyst and excess alcohol.
Drying: Heated to remove water content.
Final Product: Clean, pure biodiesel ready for testing.

## Slide 19: Fuel Quality Analysis
Properties tested: Density, Viscosity, Acid Value, Flash Point.
Meets ASTM D6751 and EN 14214 standards.
Suitable for blending or direct diesel engine use.

## Slide 20: Future scope
Using new catalysts
Experimentation with various feedstocks.
Future: Mixed-metal catalysts, continuous reactors, full life cycle analysis

## Slide 21: References
Ma & Hanna, Bioresource Tech (1999)
Demirbas, Energy Conv & Mgmt (2009)
ASTM D6751, EN 14214 Standards
More references in the report

## Slide 22: THANK YOU!